## Slide 1: Addressing Modes in Microprocessors
In all micro-processing systems there are several modes of data addressing to simplify programming in assembly language or in machine code.
There are the following most useful addressing modes:
1. Inherent; 2. Immediate; 3. Direct;
4. Relative and 5. Indexed modes

## Slide 2: Inherent Addressing Mode
Definition: Inherent addressing mode is the mode when instruction does not request any data because operation does not require that.
EXAMPLES:
1. NOP – “No operation”. This instruction is used only to pass the instruction execution cycle. It is used in assembly programming to adjust real-time program execution.
2. INX – Increment Index register “X”

## Slide 3: Addressing Modes: “Inherent”
PC = 100
CPU
MEMORY Address
Address Bus
100
INX
PC content appears on the Address BUS = 100
Content of Memory in Address = 100 goes to Instruction Register in CPU over the Data Bus
Data Bus
Instruction Reg.
INX
100
1000
Index Reg. X =
20FF
Op-Code [Increment X-Reg.] goes to ALU and content of X-reg. increments (20FF+1 = 2100)
ALU
2100

## Slide 4: Immediate Addressing Mode
Definition: Immediate addressing mode is the mode when instruction contains the operand (data) inside instruction word. Usually is used to store constants in the “body” of the program.
EXAMPLE:
1. LDAA #55 ; Load digit 55 (0101 01010) to the Reg.A in CPU

## Slide 5: Addressing Modes: “Immediate”
PC = 100
CPU
MEMORY Address
Address Bus
100
LDAA #55
PC content appears on the Address BUS = 100
Content of Memory in Address = 100 goes to Instruction Register in CPU over the Data Bus
Data Bus
Instruction Reg.
LDAA #55
100
1000
Op-Code [Load] goes to ALU and operand 55 is loaded from instruction to Reg.A in CPU
ALU
Data Reg. A
55

## Slide 6: Direct Addressing Mode
Definition: Direct addressing mode is the mode when instruction contains the address of data location.
Direct addressing mode may have “Extended Direct” mode when operand is addressed in two consecutive bytes in the range of addresses from “0000” to “FFFF”
EXAMPLES:
LDAA $1000 – “Load 8-bit data (e.g. 25) from the address $1000 to the register “A”.
LDX $2780 – “Load 16-bit data from addresses $2780 (low byte) and $2781 (high byte).

## Slide 7: Addressing Modes: “Direct”
PC = 100
CPU
MEMORY Address
Address Bus
100
LDAA $1000
PC content appears on the Address BUS = 100
Content of Memory in Address = 100 goes to Instruction Register in CPU over the Data Bus
Data Bus
Instruction Reg.
LDAA $1000
100
1000
Data Reg. A
Op-Code [Load] goes to ALU and address of the data [1000] appears on Address Bus
ALU
1000
25
The data [25] located in address [1000] goes to requested register “A” in CPU

## Slide 8: Relative Addressing Mode
Definition: Relative addressing mode is the mode when instruction include signed address offset and allows addressing memory location relative to existing (current) address. The offset can be 8 or 16 bit.
EXAMPLE:
Addr.| Instruction | Comment
0100 LDAA $1000 Load Reg.A from the address $1000
0103 INCA Increment Reg.A content
0104 BPL -4 Branch “if plus” to address = 0104 – 4= 0100

## Slide 9: Addressing Modes: “Relative”
PC = 104
CPU
MEMORY Address
Address Bus
104
LDAA $1000
PC content appears on the Address BUS = 104
Content of Memory in Address = 104 goes to Instruction Register in CPU over the Data Bus
Data Bus
Instruction Reg.
BPL -4
100
1000
Data Reg. A
Op-Code [BPL=2A] goes to ALU and address of next instruction 104 – 04=100 goes to PC
ALU
25
The new instruction address [100] is sent to the address bus and new instruction is loaded
INCA
103
104
LDAA $1000
BPL -4
PC = 100
100
The new instruction LDAA $1000 is executed by loading Reg. A with data [25] from $1000
25

## Slide 10: Indexed Addressing Mode
Definition: Indexed addressing mode is the mode when data address is calculated as sum of content of the index register and signed address offset in instruction. The offset can be: 5-bit (4 + 1 bit sign); 9 bit (8 + 1 bit sign) and 16 bit.
EXAMPLE: Content of index register X = 1000
Addr.| Instruction | Comment
100 LDAA 20, X ; Load Reg. A from the address [X] + 20
104 STAA 40, X; Store Reg. A from the address [X] + 20

## Slide 11: Addressing Modes: “Indexed”
PC = 100
CPU
MEMORY Address
Address Bus
100
LDAA 20,X
PC content appears on the Address BUS = 100
Content of Memory in Address = 100 goes to Instruction Register in CPU over the Data Bus
Data Bus
Instruction Reg.
LDAA 20, X
100
1020
Data Reg. A
Op-Code [Load] goes to ALU and address of the data is calculated as [X=1000] + 20 = 1020
ALU
1020
25
The data [25] located in address [1020] goes to requested register “A” in CPU
STAA 40, X
STAA 40, X
PC content increments to next address = 104
PC = 104
The data [25] in Reg. A is stored in memory address [X=1000] +40 = 1040
104
25
25
1040
1040
104

## Slide 12: Assembly Programming
Concepts of Programming on Assembly language:
Microprocessor performs instructions encoded in machine core. This binary
code is quite difficult for programmer . Thus, programming takes a lot of time
Programmer prefer to write a program in form of text using symbolic language (text) and digits in their symbolic form (0,1,2,…9)
Therefore, special program called Translator is needed to convert the textual
form of the program to the machine code loadable to CPU for data execution
Begin
Org $100
LDAA #55;
ADDA $1000
STAA $1100
End
0100: 86
0101: 55
0102: bb
0103; 10
0104: 00
0105: 7a
0106: 11
0107: 00
1000: 25
1100:
Assembly Language Translator

## Slide 13: Assembly Programming
Assembly Language Program Structure
Assembly language consist of:
1. Directives, 2. Instructions and 3. Comments
Definitions:
Directive is a command to the translator which informs how to process
subsequent assembly language instructions: e.g. “Begin”, “End”, “Org”, etc.
Instruction is a command to the CPU which informs processor how to
execute data or control information: e.g. LDAA #55; BPL -4, etc.
Comment is text to programmer which explains the function of the
instruction or group of instructions: e.g. Load of register A with initial value

## Slide 14: Assembly Programming
Assembly Instruction Structure
Assembly instruction consist of the following fields:
Labels are symbols defined by programmer to identify memory locations and data areas of the assembly modules. The label is optional
Operation is a field which specifies an assembler instruction, directive or a
macro call: e.g. ADDA, LDAA, EQU, etc.
Operand field is composed from one or more operands. This field is used to
supply arguments to the assembly instruction, directive or macrofunction.
Label
Operation
Operand(s)
Comment
Loop
ADDA
EXAMPLE
Comment is optional text for programmer to explain what instruction or group
of instructions does: e.g. Add 20 to content Reg. A and store result in Reg. A
#$20
Add 20 to content of Reg. A

## Slide 15: Assembly Programming
Input / Output: used to indicate input or output data
Terminals: used to indicate start or end the program
Standardized Flowchart Symbols
START
Load A
Process: used to indicate data execution process
Add A, B
Condition: used to indicate condition after operation
B>S?
Subroutine: used to indicate subroutine execution
FIR
Connectors: used to indicate logic connection in program
1
2

## Slide 16: Assembly Programming
Problem definition: Write a program to sum 3 data-elements located in memory from address $1000 and store the result in $1100
Arithmetic Functions
Start
Flowchart
Assembly program
ORG $1500 ; Start from address 1500
[A]  [1000]
LDAA $1000 ; Load A from address [1000]
[A]  [$ 1010]
[A]  [A] + [$ 1001]
ADDA $1001 ; Add A and [1001], store in A
[A]  [A] + [$ 1002]
ADDA $1002 ; Add A and [1002], store in A
STAA $1010 ; Store [A] in address 1010
END ; End of the assembly program
End