## Slide 1: Arithmetic operations Programming
Representation of digits in micro-processing systems
8-bit two’s complement
Binary sign | Binary value | Decimal sign | Decimal value
0 | 1111 1111 (max) | + | 255
0 | 0000 0001 (min) | + | 1
0 | 0000 0000 |  | 0
1 | 1111 1111 (min) | - | 1
1 | 0000 0000 (max) | - | 256

## Slide 2: Addition and Subtraction
Concept of Carry / Borrow bit:
9-th bit in 8-bit “Add” or “Subtract “operations or
17-th bit in 16-bit “Add” or “Subtract” operations is considered as a special C-bit (C-flag) in Condition Code Register (CCR)
1001 1001
0
+ $ 99
+ $ 74
0111 0100
0
-
1001 1001
0
+ $ 99
+ $ 74
1000 1011+1
1
+
0010 0101
1
0
+ $ 25
0011 1001
0
+ $ 39
+ $ 74
0111 0100
0
-
0011 1001
0
+ $ 39
+ $ 74
1000 1011+1
1
+
1100 0101
1
- $ C5
- $C5
=
0011 1010+1
+ 57
+ 116
- 59

## Slide 3: Programming the Subtraction operation
Org $1500 ; Starting address of the program
LDAA # $ 39 ; Load BCD digit $39 (0011 1001)
SBCA # $ 74 ; Subtract BCD $ 74 (0111 0100)
STAA $1001 ; Store the result in address $1001
END
Please read pp. 50 to 60: “Multi-precision operations, BCD operations and Multiplication & Division operations. Read example programs.

## Slide 4: Condition Code Register (CCR)
Condition code Register (CCR) is special purpose register which contains set of flags indicating conditions of the operation recently executed
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
 |  | H |  | N | Z | V | C
Bit 0: C-bit => Carry Flag
Bit 1: V-bit => Overflow Flag. Whenever result of a two’s compliment operation is out of range V=1
Bit 2: Z-bit => Zero Flag. Whenever result is 0 than Z=1, otherwise Z=0
Bit 3: N-bit => Whenever the most significant bit of the result of operation is = 1, than N=1, Otherwise, N=0
Bit 5: H-bit => Half-carry flag is carry flag for lower 4-bits to the upper 4 bits.

## Slide 5: Program Loops
Loop is program element for repetitive operation with determined segment of algorithm.
Definition 1: Finite loop a sequence of instructions that will be executed for finite number of times
Definition2: Endless loop a sequence of instructions that will be executed forever if started (until power off)

## Slide 6: Program Loops
Loop is program element for repetitive operation with determined segment of algorithm.
Definition 1: Finite loop a sequence of instructions that will be executed for finite number of times
Definition2: Endless loop a sequence of instructions that will be executed forever if started (until power off)